## Slide 1: Contact Information: Dr. Rich Dunk: dunk@marine.rutgers.edu Greg Seroka: seroka@marine.rutgers.edu Dr. Travis Miles: tnmiles@marine.rutgers.edu Data and Reports Available: http://rucool.marine.rutgers.edu/bpu Presentation given to RES Americas & DONG June 6, 2016
Modeling & Evaluation of New Jersey’s Offshore Wind Resource

## Slide 2: New Jersey Studies of Interest- BOEM
Ongoing:
Modeling & Evaluation of New Jersey’s Offshore Wind Resource (Rutgers Univ.)
Atmospheric/oceanic modeling of NJ Offshore Wind Lease Areas
Hourly 3D modeled wind speed 2011-present
Hi-Res Weather Model
Spatial Validation Data
Wind Power Statistics
New Ocean Data
Innovative Sea Breeze Analyses
Tropical Cyclone Modeling

## Slide 3: New Jersey Studies of Interest- BOEM
Ongoing:
Modeling & Evaluation of New Jersey’s Offshore Wind Resource (Rutgers Univ.)
Hourly kWh data, net capacity factor for hypothetical wind farm scenarios
Connections with economic models at RU CEEEP
Hi-Res Weather Model
Spatial Validation Data
Wind Power Statistics
New Ocean Data
Innovative Sea Breeze Analyses
Tropical Cyclone Modeling

## Slide 4
NJ WEA Potential Capacity >=3,000 MW
Motivation for OSW Program
Offshore wind (OSW) developers typically use annual average wind distribution + wind rose for “site suitability” and project planning
Modeling at >=20km grid spacing
Annual Average

## Slide 5
Motivation for OSW Program
NJ BPU OSW Rules require applications to include analysis of project generation during peak electricity demand and on an annual basis over twenty years.
Chart: 
Relative Load
2013-14 PJM Mid-Atl. Daily Max Load
Wind resource variations during peak electricity demand can be caused by sea breeze and intermittent coastal storm events.

## Slide 6
Sources of NJ Wind Variability
Winter Storms
Sea Breeze Circulation
Tropical Cyclones
Coastal Upwelling
Peak Energy Demand
Peak Energy Demand
Peak Energy Demand
Secondary Peak Energy Demand

## Slide 7: Rutgers University Weather Research & Forecasting (RU-WRF) Model
Run Continuously 2011 – Present
Triple nested: 9km-3km-1km
  9km: 0, 6, 12, 18Z cycles
  3km: 0, 12Z cycles
  1km: 12Z cycle (Research Mode)
Vertical Levels:
  40-42; more tightly packed near surface
Hourly forecast: out to 5 days (9km), 2 days (3km) and 1 day (1km)
Boundary Conditions:
  9km: 0.25 degree Global Forecast System
  3km: RU-WRF 9km
  1km: RU-WRF 3km
  Satellite SSTs: state-of-the-science declouded coldest pixel composite SST to resolve coastal upwelling and storm mixing
STANDARD MET VARIABLES SAVED – temperature, pressure, wind speed and direction, wind gusts, solar radiation, humidity, precipitation, etc.
9km
3km
1km
RU-WRF Domains
Notes: High Resolution
Long-time period (5 years)
Sea

## Slide 8
RU-WRF uses coldest pixel SST composite for bottom boundary conditions
  Web: http://rucool.marine.rutgers.edu/ruwrf-mesoscale-meteorological-model-forecast
Example:
8 July 2013 Upwelling
Coldest Pixel SST
RTG SST

## Slide 9
Example:
Hurricane Irene
August 2011
BEFORE IRENE
AFTER IRENE
Rutgers SST
RTG HR SST
NAM model
RU-WRF uses coldest pixel SST composite for bottom boundary conditions
  Web: http://rucool.marine.rutgers.edu/ruwrf-mesoscale-meteorological-model-forecast

## Slide 10: Coastal/Offshore Monitoring
Coastal Met Towers
Coastal SoDAR and LiDAR Remote Monitoring Systems
Coastal Radar (CODAR)
Offshore Met Monitoring Platform and Met Buoy
Notes: Fishermen: already deployed monitoring buoy, once done go to one 10 nm out
-purchased offshore vertical lidar, measure wind spd, dir, turbulence, deployed in June
-bought scanning lidar, deployed at end of summer
-bought wind tracer near Margate, see 10 nm offshore, in vertical
-2-3 60m met towers along coast, instrumented at 3 levels
Offshore Megawatt (German): no monitoring, rely on our study
Bluewater Wind: claim deploying monitoring sites at end of summer
Garden State Offshore Energy (part PSEG, part Deepwater Wind): vertical lidar on buoy, validate in Rhode Island, target this summer with LIDAR

## Slide 11
Wind Variability: Sea Breeze
RU-WRF Model Performance
14:00
17:00
20:00
23:00
September 12, 2012 10m Winds
June 19, 2014 100m Winds

## Slide 12
Wind Variability: Sea Breeze
RU-WRF Model Performance
RU-WRF Model 2km Simulation
Offshore wind direction
Onshore wind direction
Land wind direction
Wind Speed [m/s]

## Slide 13
Wind Variability: Coastal Upwelling
RU-WRF Model Performance
30-40 m
110+ m

## Slide 14
Wind Variability: Tropical Cyclones
RU-WRF Model Performance

## Slide 15
Improved OSW Analyses
Modeling at <3km grid spacing
Hourly winds
Modeling at 20km grid spacing
Annual Average
Space/time variability of wind generation captured by using the high resolution RU-WRF model.
RU-WRF
Standard

## Slide 16
Existing OSW Resource Products
Virtual Meteorological Tower Data
Wind Resource Maps
Hypothetical Wind Farm Production Data

## Slide 17
Virtual Meteorological Towers

## Slide 18: Virtual Met Tower Example
Offshore
120m
100m
80m
60m
10m
Time
Wind Speed
Notes: -Peak in wind speed at around 00Z on June 4 is higher offshore than onshore, from surface up to 100m; at 120m, wind speed is comparable offshore to onshore (less frictional drag)

## Slide 19
Virtual Met Tower (VMT) Data
Average Monthly and Annual Wind Speeds (m/s) are derived from the mean hourly wind speed for each day of the month @80, 90, 100, 110, 120m for each of the 45 VMTs. Additionally, hourly met data including most standard meteorological parameters are available for every day of the year (8760 hrs) at the selected VMT heights.
…
…

## Slide 20
Virtual Met Tower Data
12X24: @80, 90, 100, 110, 120m
8760
Wind Roses: annual, monthly
Jan
Feb…
Dec

## Slide 21
Wind Resource Maps
80, 90, 100, 110, 120m
Annual, Seasonal, Monthly
…

## Slide 22
Hypothetical Wind Farm Production Data
Scenarios: 1100, 2000, 3000 MW; 8X10, 10X12, 10X15
Data: Hourly wind speed, kWh, capacity factor aggregated across hypothetical wind farm
North Zone
South Zone
6 MW WTG

## Slide 23: Other OSW Resource Products
Spatial predictions of Gross Capacity Factor
100m Hourly Gross Capacity Factor
during a sea breeze event

## Slide 24
RU-WRF: A Multi-Use Hourly Wind Model
Hourly net production provided to RU CEEEP for economic analyses
Model can also be used for operational forecasting for:
  Severe weather forecasting for construction, O&M
  PJM grid management
  Energy market trading

## Slide 25: Ongoing/Proposed OSW Studies
Lagrangian Coherent Structures (LCS) for offshore sea breeze clarification
Sediment transport and resuspension
Hurricane intensity
LCS for Sea Breeze (red=divergence, blue=convergence)

## Slide 26: Ongoing/Proposed OSW Studies
Data assimilation
Coupled ocean-atmosphere-wave modeling
Large Eddy Simulation (LES) for coastal/offshore turbulence estimations:
Virtual met tower data used to derive turbulence intensity, wind shear, & atmospheric boundary layer stability at heights representative of OSW WTG dimensions
Hypothetical 1000MW wind farm analysis for the BOEM NJ WEA using “new” generation OSW WTGs with higher efficiencies, power ratings, and hub heights >110m.

## Slide 27: Modeling & Evaluation of New Jersey’s Offshore Wind Resource Contact Information: Dr. Rich Dunk: dunk@marine.rutgers.edu Greg Seroka: seroka@marine.rutgers.edu Dr. Travis Miles: tnmiles@marine.rutgers.edu Data and Reports Available: http://rucool.marine.rutgers.edu/bpu
Contact Info & Data Link